## Slide 1
Air
3) Make/check ddscat.par file in “spheres_website” folder
4) Make/check gold.tab file
5) In the terminal, run ddscat by typing ./ddscat7.1/src/ddscat
Au
60 nm
a_eff = 30 nm
Dipole spacing (d) = 2 nm
Wavelength of interest = 450 to 600 nm
0 = IWRPOL
3.00e-3 = GAMMA
Create a file with the dielectrics of Au
2) Compile the source in spheres_website/ddscat7.1/src/ : by typing 1) “make clean” and 2) “make all” in your terminal (cygwin/linux)
1) Extract and go to “spheres_website” folder
Find the peak wavelength of scattering/extinction
6) Delete *.avg files they are of no use in our case
7) Rename “qtable” to “scat_and_abs.dat”.
Examine “scat_and_abs.dat” file for the peak extinction/scattering.
x
y

## Slide 2
1) Make/check ddscat.par file in “spheres_website” folder
2) Make/check gold.tab file
3) Run ddscat by typing ./ddscat7.1/src/ddscat
Everything same as in previous page but,
Wavelength of interest = peak extinction wavelength (0.512 micron) 1 = IWRPOL
Create a file with the dielectrics of Au
Calculate polarization file
for electric field distribution
4) Delete all avg, qtable,qtable2,mtable files for cleaning up. They are of no use now.
5) Make/check ddfield.in
This file has x,y,z values defining a region of xrange= [-50,50] and yrange=[-50,50] for every 1d (2 nm), so n=101
6) Run ddscat by typing ./ddscat7.1/src/ddfield.exe
This creates
7) Run ddscat by typing ./ddscat7.1/src/ddfield.exe
8) To visualize the fields, run matlab_plotter.m in matlab
Define a x,y plane here
9) Check for efield.png